## Slide 1
1
What We Have Working
Hourly 3-class XGBoost at NESTOR-BES · Primary production system · Active
Tijuana River Valley H₂S Prediction · Model Status · June 2026
Model
› Single XGBoost trained on NESTOR-BES observations
› 43-feature input: weather, wind, flow, H₂S lags, SBIWTP, atmospheric stability
› Three output classes: Green (<5 ppb) · Yellow (5–30 ppb) · Orange (≥30 ppb)
› hour_sin/cos + stable_atm + is_night — model sees time-of-day signal
› Ongoing retraining via Dagster hourly pipeline
Performance
Orange recall: 61.3 %
False alarm rate: 5.4 %
Night (20h–06h): Higher recall — most events are nocturnal
Day (06h–20h): Lower recall, consistent FAR — not day-blind
3-class benefit: Yellow captures moderate events a binary split misses
Known Limits
› NESTOR-BES only — no outputs for IB CIVIC CTR or SAN YSIDRO
› No lead-time resolution — same model weights used at 0 h and 24 h ahead
› Multi-horizon pipeline is built (36 models, 3 stations, 4 horizons) but STOPPED — needs out-of-season validation before restart

## Slide 2
2
What We Fixed
Tiered alert system (T1–T3) · Complete collapse Apr–May 2026 → Repaired 2026-06-02
Tijuana River Valley H₂S Prediction · Model Status · June 2026
The Collapse
Month
% fired
Real H₂S?
Feb 2026
5.5 %
yes
Mar 2026
15.5 %
yes
Apr 2026 ▼
0.0 %
48 ppb avg
May 2026 ▼
0.0 %
13 ppb avg
Root causes
› SBIWTP hard gate: plant at surplus all spring → anomaly ≥ 0 → entire alert chain dead
› SBIWTP weights 5–9× too large → surplus pushed score down
› quiet_night_stats were placeholders — sbiwtp_anomaly std 22× inflated
The Fixes (v4 config, 2026-06-02)
› Gate: SBIWTP deficit prerequisite replaced by met-data availability (wind_speed_10m not NaN)
› Weights re-derived from Oct 2024–Jun 2026 full dataset (Cohen's d): sbiwtp_flow −1.44 → −0.24 flow_log sign flip → +0.38 stable_atm → +0.50 | wind_speed remains −0.54
› Tier 1 expanded: atmospheric features added so calm/stable nights unlock the chain even with no SBIWTP deficit
› quiet_night_stats calibrated from 1,230 real quiet-night rows — sbiwtp_anomaly std 3.5 → 0.16
Recall Before → After (Tier 3)
Month
Horizon
Before
After
Apr 2026
nowcast
0.08
0.54
Apr 2026
mid
0.08
0.45
Apr 2026
day-ahead
0.07
0.29
May 2026
nowcast
0.00
0.48
May 2026
mid
0.00
0.41
May 2026
day-ahead
0.00
0.24
All months
nowcast
0.23
0.35
System no longer collapses on atmospheric-driven events.

## Slide 3
3
What's Left
Remaining gaps after the fix · Open work items · Path to broader coverage
Tijuana River Valley H₂S Prediction · Model Status · June 2026
Gap 1 — Daytime alerting
› Zero fires on daytime hours in Apr/May 2026 — fix did not help daytime
› Sea breeze raises wind speed above 4.0 m/s gate during daylight — gate never passes
› Daytime H₂S events driven by different mechanisms than nocturnal
› Needs separate daytime gate thresholds or a parallel daytime scoring path
› Left as future work — requires labeled daytime event dataset to calibrate
Gap 2 — Tiered system maturity
› Design acceptance targets (§6.1) not yet met
› Need ≥2 years of labeled events for robust threshold tuning
› quiet_night_stats must be regenerated after each dataset refresh (uv run python -m h2s.defs.tiered_alerts.backtest --emit-stats) → add to operational runbook
› NB fallback to IB CIVIC CTR implemented but unvalidated during outages
Gap 3 — Single-station scope
› Hourly model: NESTOR-BES only — no IB CIVIC CTR or SAN YSIDRO
› No lead-time resolution — 0 h and 24 h use identical weights
› Multi-horizon pipeline built: 36 models, 3 stations, 4 horizon buckets
› STOPPED — trained on Nov 2023–Apr 2026 only, no out-of-season validation
› Path: accumulate May–Oct 2026 data, validate seasonal generalization, then restart